## Slide 1
IP4-15: A Low Overhead Error Confinement Method based on Application Statistical Characteristics
M. Sc. Zheng Wang (wangz@ntu.edu.sg)  Dr.-Ing. Anupam Chattopadhyay (anupam@ntu.edu.sg)  Dr. Georgios Karakonstantis (G.Karakonstantis@qub.ac.uk)
Statistical Error Confinement
Architecture Extension
Example: JPEG application
Memories are usually protected by ECC
  Large overhead for error detection / correction
  Prevalent SECDED code only correct single bit error
Custom instructions | Functionalities
set_data @{start} @{size} @{lut_start} @{lut_size} | Register protected data array and the LUT of statistic data
enable_parity | Turn on store protection
disable_parity | Turn off store protection
chk_ld @{dst} @{src} @{offset} | Return statistical data in @{dst} if an error is detected in @{src}
DATA
MEM
FE_DC
FETCH
ALU_DC
SEC_DC
ALU_EX
BRA_EX
LDST
MEM
MEMORY INTERFACE
REGISTER FILE
MEMORY
ACCESS
DC_EX
EX_MEM
MEM_WB
PRE
/FE
EX
MEM
WB
DC
PROG
MEM
BRA_DC
CTRL_DC
TRAP_DC
LDST_DC
Data flow
SEC_EX
SEC_MEM
SEC_WB
LDST_EX
Gen_parity
WRITE
BACK
SEC_REG
int imageEx[SIZE][SIZE];
int imageData[ROW_SIZE][COL_SIZE];
int imageExtended[ROW_SIZE][COL_SIZE];
// reference LUT containing generalized data
int lut_imageEx[8][8]={{780, -1, 0, 1, 0, 0, 0, 0 },
{ 0, 0, 0, 0, 0, 0, 0, 0 },
{ 0, 0, 0, 0, 0, 0, 0, 0 },
{ 0, 0, 0, 0, 0, 0, 0, 0 },
{ 0, 0, 0, 0, 0, 0, 0, 0 },
{ 0, 0, 0, 0, 0, 0, 0, 0 },
{ 0, 0, 0, 0, 0, 0, 0, 0 },
{ -2, 0, 0, 0, 0, 0, 0, 0 }};
int DiscreteCosine(int imageData[SIZE][SIZE], int imageEx[SIZE][SIZE])
{ ......
asm("enable_parity"); // turn on store protection
imageEx[i1][j1]= (int)sum;
asm("disable_parity"); // turn off store protection
.......
}
int Quantization(int imageEx[SIZE][SIZE], int imageExtended[SIZE][SIZE])
{ ......
int src = imageEx[i1][j1];
int dst;
asm("check_value @dst, @src, index"); // automatic correction
imageExtended[i1][j1]= (dst/quant[i][j]);
......
}
int main()
{ ......
// register range of protected data using reference LUT
asm("set_data @imageEx, 262144, @lut_imageEx, 64");
DiscreteCosine(imageData, imageEx);
Quantization(imageEx, imageExtended);
......
}
Programming example for JPEG application
Architecture extension for RISC processor
(c) 100 errors
PSNR 39.12 dB
Protected
(d) 500 errors
PSNR 38.51 dB
Protected
(e) 800 errors
PSNR 36.24 dB
Protected
(f) 1000 errors
PSNR 23.68 dB
Protected
(b) 100 errors
PSNR -89.94 dB
No protection
(a) 1 error
PSNR -0.03 dB
No protection
Fault injection experiment (single bit-flip errors)
Chart: Number of injected single bit-flips to DCT coefficients
| 0 | 1 | 10 | 100 | 500 | 700 | 800 | 900 | 1000
Error Confinement | 39.22 | 39.22 | 39.22 | 39.12 | 38.51 | 36.42 | 36.24 | 23.68 | 23.68
ECC | 39.22 | 39.22 | 39.22 | 39.22 | 39.22 | 39.22 | 39.18 | 23.53 | 23.53
No Protection | 39.22 | -0.03 | -84.33 | -89.94 | -97.26 | -98.64 | -98.91 | -99.16 | -99.74
(a)
Chart: Number of faulty bits of multiple bit-flips (100 errors to DCT coefficients)
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
Error Confinement | 39.22 | 39.12 | -91.57 | 39.19 | -95.69 | 39.17 | -96.45 | 38.93 | -97.29 | 38.23 | -98.69
ECC | 39.22 | 39.22 | -93.31 | -92.91 | -95.4 | -95.59 | -96.19 | -97.26 | -97.36 | -97.57 | -98.75
No Protection | 39.22 | -89.94 | -91.57 | -92.58 | -95.69 | -95.35 | -96.45 | -97.13 | -97.29 | -97.57 | -98.69
(b)
Chart: Benchmark of execution time with ECC w.r.t. various image size
| 8x8 | 16x16 | 32x32 | 64x64 | 128x128 | 256x256 | 512x512 | 1024x1024
Proposed | 27 | 29 | 30 | 33 | 57 | 143 | 488 | 1881
ECC | 30 | 31 | 32 | 55 | 132 | 433 | 1594 | 6554
Chart: Benchmark of data memory usage w.r.t. various image size
| 8x8 | 16x16 | 32x32 | 64x64 | 128x128 | 256x256 | 512x512 | 1024x1024
Proposed | 264 | 288 | 384 | 768 | 2304 | 8448 | 33024 | 131328
ECC | 48 | 192 | 768 | 3072 | 12288 | 49152 | 196608 | 786432
(c)
(d)
Error resiliency and performance overheads
DCT
Quantization
De-quantization
IDCT
Statistical mean matrix (8 X 8 elements)
of DCT coefficients
Statistical mean matrix (8 X 8 elements)
of quantization coefficients
Alternative: applications with statistical properties
  DSP applications e.g. JPEG
Statistical error confinement
Simple parity bit for error detection
Substitute erroneous value by statistical mean
Confine error effects with low overheads
Limit error effects for multiple bit-flip errors
Architecture support
Programming model for generic algorithms
Custom instructions for RISC style processor
Synthesizable processor architecture