## Slide 1
IP4-15: A Low Overhead Error Confinement Method based on Application Statistical Characteristics
M. Sc. Zheng Wang
Dr. -Ing Anupam Chattopadhyay
Dr. Georgios Karakonstantis Queen University Belfast

## Slide 2: Statistical Error Confinement
Memories are usually protected by ECC
  Large overhead in size and power for error detection/correction
  Prevalent code can only correct single bit error
Applications existing statistical data distributions
  DSP applications e.g. JPEG
  Simple parity bit for error detection
  Substitute erroneous value by statistical data in LUT
  Able to confine errors (single and multiple bit errors)
DCT
Quantization
De-quantization
IDCT
Statistical mean matrix of DCT coefficients
Statistical mean matrix of quantization coefficients

## Slide 3: Statistical Error Confinement – Experiments
(c) 100 errors
PSNR 39.12 dB
Protected
(d) 500 errors
PSNR 38.51 dB
Protected
(e) 800 errors
PSNR 36.24 dB
Protected
(f) 1000 errors
PSNR 23.68 dB
Protected
(b) 100 errors
PSNR -89.94 dB
No protection
(a) 1 error
PSNR -0.03 dB
No protection
Refer to paper/poster for benchmarking with ECC protection

## Slide 4: Statistical Error Confinement – ASIP
Architecture extension on RISC processor
Custom instructions | Functionalities
set_data @{start} @{size} @{lut_start} @{lut_size} | Register protected data array and the LUT of statistic data
enable_parity | Turn on store protection
disable_parity | Turn off store protection
chk_ld @{dst} @{src} @{offset} | Return statistical data in @{dst} if an error is detected in @{src}
DATA
MEM
FE_DC
FETCH
ALU_DC
SEC_DC
ALU_EX
BRANCH_EX
LDST
MEM
MEMORY INTERFACE
REGISTER FILE
MEMORY
ACCESS
DC_EX
EX_MEM
MEM_WB
PRE/FE
EX
MEM
WB
DC
PROG
MEM
BRANCH_DC
BYPASS_DC
TRAP_DC
LDST_DC
Data flow
SEC_EX
SEC_MEM
SEC_WB
LDST_EX
Gen_parity
WRITE
BACK
SEC_REG